# Project Apex II – Technical Design Document (Jon Sowman – April 2011)
### Custom Data Format

We have the following data available to the flight computer via various sensors etc, that we will transmit via telemetry:

- Number of GPS satellites in view
- Internal & external temperature
- Barometric Pressure
- Battery Voltage
- IRD 1&2
- Light Sensor
- RSSI (1)

We are using the standard UKHAS format for the main telemetry packets:
$$<CALL SIGN>,<COUNTER D>,<TIME HH:MM:SS>,<LATITUDE DD.DDDDDD>,<LONGITUDE DD.DDDDDD>,<ALTITUDE METRES MMMMM>,
<O SPEED KM/H DDDD.DD>,<O BEARING DDD.DD>,
<O TEMPERATURE INTERNAL C D.DD>,<O TEMPERATURE EXTERNAL C D.DD>,
<O TEMPERATURE CAMERA C D.DD>,
<O BAROMETRIC PRESSURE hPa(millibars)>,<O CUSTOM DATA>*<CHECKSUM><NEWLINE>

Given this, we will use the following format for the Apex II telemetry:
$$APEX,<TICKS>,<TIME>,<LAT DDMM.MM>,<LON DDMM.MM>,
<ALT MMMMM>,<SPEED DDD>,<BEARING DDD>,<SATS DD>,
<INT_TEMP>,<EXT_TEMP>,<PRESSURE HHH>,<BATT_VOLTS HHH>,
<IRD_1 HHHH>,<IRD_2 HHHH>,<LIGHT HHHHHHHHH>,
< RSSI HH>*<CHECKSUM HHHH>
### Formatting
- Temperature: dd.dd variable length, two decimal points, degrees Celcius
  - Always two decimal places, but can be positive or negative variable length
- Pressure: hhhh fixed length hexadecimal
  - 12 bit ADC referenced to 5 Volts
  - data = 10 * (((data / 4096) * 5) + 5 * 0.095) / (5 * 0.009)
- Battery voltage: hhhh fixed length hexadecimal
  - 12 bit ADC referenced to 5 Volts
- IRDs: hhhh fixed length hexadecimal
  - Counts in the last 30 seconds
- Light: hhhhhhhh fixed length hexadecimal
  - Concatenated red, green, blue and white values, followed by a multiplier
  - rrggbbwwm
- RSSI: hh fixed length hexadecimal
  - 8 bit ADC referenced to 3V3